## Slide 1: Molecular luminescence FLUORiMETRY AND PHOSPHORIMETRY
luminescence
phosphorescence
chemoluminescence
photoluminescence
fluorescence
radioluminescence
Radiation due to temperature = incandescence
All other form of light emission is called as luminescence

## Slide 2: What makes a compound UV active?
Ones that do are said to be 'UV-active' and ones that do not are 'UV-inactive'.
To be UV-active compounds must possess a certain degree of conjugation, most commonly aromatic compounds.

## Slide 3: What are fluorescent compounds?
A fluorophore (or fluorochrome, similarly to a chromophore) is a fluorescent chemical compound that can re-emit light upon light excitation.
Fluorophores typically contain
several combined aromatic groups,
or planar
or cyclic molecules with several π bonds

## Slide 4: Principles of Fluorescence
Energy level diagram (Jablonski diagram)

## Slide 5: Energy level diagram (Jablonski diagram)

## Slide 6: FLUOROSENCE QUENCHING
Self quenching or concentration quenching:
Chemical quenching : (due to pH,O2,halides, heavy metals)
Static quenching : (complex formation, caffeine as quencher for riboflavin)
Collision quenching:(Halide, heavy metals, Increase in temperature, decrease in viscosity)

## Slide 7: Factors affecting the fluorescence
Nature of the molecule: able to absorb uv or visible radiation
2. Nature of the substituent‘s (electron donating group, electron donating group, SO3H, NH4, alkyl group OH NH2 &
withdrawing gp COOH,NO2, Halides, C=O)
3. Polarity
4. Effect of PH;
(ANILINE Alkali pH; ---visible fluorescence, acidic—uv fluorescence
PHENOLS: alkali: fluorescence, acidic : no fluorescence,
5. Effect of dissolved gasses (it oxidizes fluorescent to non fluorescent )

## Slide 8
6. Temperature
7. Effect of structural rigidity
8. Quantum efficiency
9.Atomic number( phenol=18, toluene=17, benzene = 10)
10. Photochemical decomposition (due to polychromatic light, no fluorescence)
11. Formation of metal complex

## Slide 9: Nature of the substituents

## Slide 10: . Effect of structural rigidity
QUANTUM EFFECIENCY= 0.2 1.0
QUANTUM EFFECIENCY = NUMBER PHOTON EMITTED
------------------------------------------
NUMBER OF PHOTON ABSORBED

## Slide 11: Quantum efficiency
Quantum yield:
the ratio of the number of molecules that luminescence to the total number of excited molecules.
f = kf/ (kf + ki + kec + kic + kpd + kd)
kf: Fluorescence constant
ki: Intersystem crossing constant
kec: External conversion constant ( deactivation of excited electronic state , b/w solvent & solutes)
kic: Internal conversion constant ( intermole process mole—lower electronic state without emission of radiation)

## Slide 12
kpd: Pre dissociation constant ( due to internal conversion electrons move from higher ES to upper vibrational state of lower ES where energy is low)
kd: Dissociation constant ( after absorption chromophoric electrons directly to higher vibrational level----- rupture of bonds)

## Slide 14: Formation of metal complex
Increase in fluorescence of chelating agents, when they complexed with a metal due to rigidity:
Ex: 8 hydroxy quinoline AND hydroxy quinoline zinc complex

## Slide 15: Fluorescence measurement
Filter fluorimeters
Spectrofluorometers
Fluorescent microscopes
Fluorescent scanners &
Flow cytometry
Notes: diffraction grating monochromators
Flow cytometry is a technique for counting, examining, and sorting microscopic particles suspended in a stream of fluid

## Slide 16: instrumentation
Components of a fluorometer:
Light sources; (mercury and xenon lamp)
wavelength selection: ( filters and monochromators)
detectors; photomultiplier tube (PMT)
sample cell.
Recorders;

## Slide 17: Block diagram of fluorometer
sample
emission monochromator
detector
source
excitation monochromator
Read-out

## Slide 18: Spectrofluorometer

## Slide 19: Spectrofluorometer

## Slide 20: source
Mercury vapour lamp: metallic arc they are designed to operate at high temperature and low pressure the emission of the lamp is at wavelength at 365, 398, 436, 546,579,690 & 734 nm
Low pressure lamps: equipped with a silica envelop provide the additional radiation at 254nm

## Slide 21
Xenon lamp : produce a radiation by the passage of current through an atmosphere of xenon.
Tungsten lamp: to produce a strong excitation band above 450
Hydrogen & deuterium arc lamp: not employed because they are not intense

## Slide 22
Filter and monochromators: (absorption + interference filters + gratings)
Detector: PMT
Cells cell compartment: cylindrical, rectangular, made up of silica or glass, they are designed to reduce amount of scattered radiation reaching the detector
Baffles: to prevent the scattered light

## Slide 23: Components of a fluorometer of a spectro-fluorometer.

## Slide 24
typical fluourometer

## Slide 25: spectrofluorometer.

## Slide 26: application
Determination of uranium salts by fluorometer
Determination of inorganic salts
Fluorescent indicators
Fluorometric reagent
Aromatic structure
Organic analysis
Pharmaceutical analysis
Determination of thiamine

## Slide 27
Determination of riboflavin
Determination of quinine sulphate
Determination of tetracycline in serum
Special application:
Investigation of chemical structure and process
Chemical analysis
Detection of impurities
Estimation of single component

## Slide 28
Determination of uranium salts by fluorometer
Uranium + HNO3 -------- oxidation + NaF
Determination of inorganic salts ( transition elements)
Not exhibit the fluorescence with non fluorescence organic molecule :
Ex:, ruthenium ions + 5 methyl 1,10 PTL ---- complex ----- fluorescence
cadnium + 2 OH phenyl benzoxazole + glacial acetic acid -- blue fluorescence

## Slide 29
Fluorometric reagent:
used for cation metal ion analysis Ex: , flavanol
Aromatic structure: determination of two or more functional group
Ex: benzoin and 8 hydroxy quinoline

## Slide 30
Fluorescent indicators:
Used in acid base titration specially for coloured substances.
Eosin : pH: 3-4 : color less to green
Fluorescein : pH: 4-6 : color less to green
Quinine sulphate: pH: 3-5 : blue to violet
2-napthaquinone pH: 4.4-6.3 :blue to colour less

## Slide 31
Organic analysis:
Determination of many organic compounds present in cigrate, smoke, automobile exhaust.
Ex: benzopyrene

## Slide 32
Pharmaceutical analysis:
Compound converted to fluorescent products by chemical reaction.
excitation emission
hydrocortisone: ethanol : 460 520
Nicotinamide : cyanogen 250 430
Reserpine : oxidation 250 430

## Slide 33
Determination of thiamine vitamin B1
( it is non fluorescent on oxidation produce florescence)
Method: sample is treated with phosphatase ------- brings the (hydrolysis of PO4 ester of thiamine) ------ filtration
( remove PO4 + insoluble matter) ------- dilute to known volume with water -------
divide into 2 group-----
one is used as blank -----
to another add NaOH + alcohol ------ + potassium ferricyanide ( oxidizing agent) + on shaking
( alcoholic extraction is separated from aqueous layer) ------ examined in fluorometer

## Slide 34
Determination of riboflavin
Treat with acid + KMNO4 (OA) ----- FA
Add sodium dithionate ----- measure the fluorescence intensity (FB)
standard substance ---- measure the fluorescence intensity (FC)
Measure the concentration of fluorescent material
FB-FA mx
--------- = -------- = mass of riboflavin in sample + standard
FC-FA mx+ ms

## Slide 35
Determination of quinine sulphate
quinine sulphate in 0.1N H2SO4 --- on serial dilution --- measure the fluorescence--- by plotting the graph
fluorescence v/s concentration

## Slide 36
Determination of tetracycline in serum
Tetracycline is converted to anhydrotetracyclin ------------fluorescence (quantum yield is less)----- on subsequent complexation with aluminum ---- fluorescence with increase sensitivity
Special application:
Investigation of chemical structure and process
Hydrogen bonding , cis-trans isomers, polymerization, tautomersim

## Slide 37
Chemical analysis: quantitative and qualitative analysis
Detection of impurities:
Cyclohexane ------ purified until it shows no trace of benzene at 2600AO
Estimation of single component ----- vitamin A

## Slide 38
Fluorescence and Phosphorescence

## Slide 39
Comparison of Fluorescence and Phosphorescence
Fluorescence Phosphorescence
life time short, < 10-5s long, several seconds
electron spin no yes
excited states singlet triplet
quantum yield high low
temperature most temperature low temperature more likely
Resonance fluorescence: absorbed radiation is re-emitted without a change in frequency.
Stokes shift: molecular fluorescence bands are shifted to wavelengths that are longer than the resonance line.

## Slide 40
Luminescence:
Energy diagram and basic concepts
2. The factors affect fluorescence
3. Excitation and emission spectra
4. Instrumentation
5. Applications

## Slide 41
Effect of Concentration on Fluorescence Intensity
F = K’ (I0 –I)
Power of fluorescence emission F
I0 and I are the intensities of excitation lights before and after absorbed by the analytes. K’ is the constant
related to the quantum yield
I/I0 = 10-ebc
F = K’ I0 (1–10-ebc)
F = 2.3 K’ I0 ebc, (when ebc<0.05)